## Slide 1: Video Contrast and Sharpness Enhancement
T. Petersen, T. C. Mol, E. Cozza
16/02/2024

## Slide 2
Satellite Imaging
Medical Imaging
AI and Computer Vision applications
Multimedia applications
Fields of Application
Satellite image
MRI

## Slide 3
Design Modules
Contrast Enhancement module
Convolution with sharpener filter
Software Implementation
Hardware Implementation
Contrast
Enhancement
Sharpening
input stream
output stream

## Slide 4
Software Implementation
01

## Slide 5: Contrast Enhancement
    Image decomposition into 3 channels
    Histogram Computation
    Adjust the brightness level of all the pixels:
    Repeat steps 2-5 for each channel
    (p is a user-defined input parameter)
th
first
last

## Slide 6: Edge Enhancement
Based on the convolution operation for a fixed kernel
where:
  ω(i;j) is the sharpener filter
  f(x,y) is the input image pixel in coordinates (x;y)
  g(x,y) is the output image pixel in coordinates (x;y)
Sofware Implementation:
Identity
Edge Detection
Sharpen

## Slide 7
Results
Original Picture
Contrast Enhancement
Contrast Enhancement + Sharpening

## Slide 8
Results
Original Picture
Contrast Enhancement
Contrast Enhancement + Sharpening

## Slide 9: Results
Module | Processing time [s/frame] | Frame Rate [frame/s]
Contrast Enhancement | 0.977 | 1.024
Edge Enhancement | 0.218 | 4.588
Total Pipeline | 1.233 | 0.811
Time measurements were recorded for each call to both the contrast and edge enhancement functions during the transmission of 60 frames.
The performances of the final design have been evaluated in terms of (average) processing time per frame and (average) frame rate.

## Slide 10
Hardware Implementation
02

## Slide 11
    Constraint:
    Acquisition, processing, and output of 1 pixel per clock cycle
    Limitations:
    Working on entire frames would require:
        Too much memory
        Too much latency
      Solution:
      Stream-Processing approach
      Exploit similarities among contiguous frames

## Slide 12: Contrast Enhancement
Synchronization of computation steps by mean of a pixel counter
Two exclusive phases:
Pixel Pipeline:
            Each received pixel increments the histogram count
            Apply contrast enhancement according to the parameters evaluated for the previous frame
            This phase involves 99.94% of all the frame pixels
Parameters Update:
          Reset: reset all the parameter concerning the previous frame
          Max: find the maximum value of the histogram for each channel
          Th: calculate the threshold
          F&L: find first and last
          PU: update all the parameters to be used for the next frame.
          This phase involves only a portion of the last row of the frame
Reset
Max
Th
F&L
PU
Pixel Pipeline
Frame structure depicting the different processing phases.
Top-level diagram of the contrast enhancement module.

## Slide 13
Results
Original Picture
Contrast Enhancement
Contrast Enhancement + Sharpening

## Slide 14
Results
Original Picture
Contrast Enhancement
Contrast Enhancement + Sharpening

## Slide 15: Results
    Processing Time:
    Frame Rate:
    Latency:
Module | Estimated Clock Period | Pipeline Stages
Contrast Enhancement | 4.961 ± 1.89 ns | 43
Edge Enhancement | 5.081 ± 1.89 ns | 8
Pixel per Frame | 921600
Target Clock Period | 7 ns

## Slide 16: Conclusion
Hardware solution is approximately 190 times faster than the software implementation.
Hardware solutions require much more design effort with respect to their software counterparts.
Possible approximation errors due to the adoption of fixed point data formats in the hardware solution.
Software Implementation
Hardware Implementation
Original Picture
Contrast Enhancement
Edge Enhancement

## Slide 17: Thank you for your attention
T. Petersen, T. C. Mol, E. Cozza